## Slide 1: Basic Concepts of IEC 61499
presented at: Distributed Automation 2000 Magdeburg, Germany 2000-03-22
by: JAMES H. CHRISTENSEN , Ph.D. IEC 61499 Project Leader Senior Principal Engineer Rockwell Automation JHChristensen@ra.rockwell.com

## Slide 2: The Challenge of Agile Manufacturing
Past: The Vision (Iacocca Institute, 1991)
  Production to Order
  Lot/Batch size > 1 Unit
  Information intensive
  "Reprogrammable, reconfigurable, continuously changeable"
Present: The Reality
  Production to Order Possible
  Order-to-delivery delay: 3-6 months(cars), 1 week (PCs)
Near Future
  Japanese Vision: "3-day car"
  Toyota/Canada (planned): "5-day car" (limited customizability)

## Slide 3: The Challenge to Automation Systems
Agility Requires Dynamic Reconfiguration!
Physical Reconfiguration
  Requires Distributed Automation
Logical Reconfiguration
  Dynamic Reorganization of Control Plans
  Minimum Human Intervention (zero preferred)
  Maintain Configuration Control
Not just Parameterization!
  Leads to Large, Complex Software Modules
  Reduces Distributability, Flexibility, Reliability

## Slide 4: Distributed Automation: An Architectural Dialectic
distributability
agility
programmability
agility
agility
distributability
configurability
programmability
Agile
Manufacturing
Function Blocks
IEC 61499
PLC IEC 61131-3
Centralized
Programmable Configurable
DCS
IEC 61804
Distributed
Configurable
Thesis
Antithesis
Synthesis

## Slide 5: Issues in the Architectural Dialectic
Execution scheduling
Communication/execution interaction
Response time requirements
Alternative algorithm selection
State machine design
Software encapsulation and reuse
Agility ( Dynamic Reconfiguration)

## Slide 6: Function Blocks in the IEC 61131-3 Context
CONFIGURATION
RESOURCE
TASK
TASK
PROGRAM
PROGRAM
FB
FB
RESOURCE
TASK
TASK
PROGRAM
PROGRAM
FB
FB
GLOBAL and DIRECTLY
ACCESS PATHS
REPRESENTED VARIABLES
Communication function
Notes: The basic high-level language elements and their interrelationships are illustrated above. These consist of elements which are programmed using the languages defined, that is, programs and function blocks; and configuration elements, namely, configurations, resources, tasks, global variables, and access paths, which support the installation of programmable controller programs into programmable controller systems.
A configuration is the language element which corresponds to a programmable controller system. A resource corresponds to a "signal processing function" and its "man-machine interface" and "sensor and actuator interface" functions (if any). A configuration contains one or more resources, each of which contains one or more programs executed under the control of zero or more tasks. A program may contain zero or more function blocks or other language elements as defined.
Configurations and resources can be started and stopped via the "operator interface", "programming, testing, and monitoring", or "operating system" functions. The starting of a configuration shall cause the initialization of its global variables according to the standard, followed by the starting of all the resources in the configuration. The starting of a resource shall cause the initialization of all the variables in the resource, followed by the enabling of all the tasks in the resource. The stopping of a resource shall cause the disabling of all its tasks, while the stopping of a configuration shall cause the stopping of all its resources.
Programs, resources, global variables, access paths (and their corresponding access privileges), and configurations can be loaded or deleted by the "communication function". The loading or deletion of a configuration or resource shall be equivalent to the loading or deletion of all the elements it contains.
Access paths and their corresponding access privileges are defined in this standard.
The mapping of the language elements defined in this subclause onto communication objects is defined in IEC 1131-5.

## Slide 7: Function Blocks in the IEC 61804 Context (Physical View)
Control Room
PC
H1 Fieldbus
Segment # 1
H1 Fieldbus
Segment # 2
CV-101
A/O
IP
102
20
19
21
AT
107A
LT
101
AT
107B
TT
105
AT
106
Re-Burned
Lime
LT
108
Purchased
Lime
LT
112
Green
Liquor
Storage
IP
104A
IP
104B
Heater
Cooler
LT
111
SC
111
SC
112
SC
108
DT
109
FT
110
SC
110
TT
104
FT
102
AT
103
24
25
23
22
H1 Fieldbus
Segment # 3
Notes: The basic high-level language elements and their interrelationships are illustrated above. These consist of elements which are programmed using the languages defined, that is, programs and function blocks; and configuration elements, namely, configurations, resources, tasks, global variables, and access paths, which support the installation of programmable controller programs into programmable controller systems.
A configuration is the language element which corresponds to a programmable controller system. A resource corresponds to a "signal processing function" and its "man-machine interface" and "sensor and actuator interface" functions (if any). A configuration contains one or more resources, each of which contains one or more programs executed under the control of zero or more tasks. A program may contain zero or more function blocks or other language elements as defined.
Configurations and resources can be started and stopped via the "operator interface", "programming, testing, and monitoring", or "operating system" functions. The starting of a configuration shall cause the initialization of its global variables according to the standard, followed by the starting of all the resources in the configuration. The starting of a resource shall cause the initialization of all the variables in the resource, followed by the enabling of all the tasks in the resource. The stopping of a resource shall cause the disabling of all its tasks, while the stopping of a configuration shall cause the stopping of all its resources.
Programs, resources, global variables, access paths (and their corresponding access privileges), and configurations can be loaded or deleted by the "communication function". The loading or deletion of a configuration or resource shall be equivalent to the loading or deletion of all the elements it contains.
Access paths and their corresponding access privileges are defined in this standard.
The mapping of the language elements defined in this subclause onto communication objects is defined in IEC 1131-5.

## Slide 8: Function Blocks in the IEC 61804 Context (Logical View)
Notes: The basic high-level language elements and their interrelationships are illustrated above. These consist of elements which are programmed using the languages defined, that is, programs and function blocks; and configuration elements, namely, configurations, resources, tasks, global variables, and access paths, which support the installation of programmable controller programs into programmable controller systems.
A configuration is the language element which corresponds to a programmable controller system. A resource corresponds to a "signal processing function" and its "man-machine interface" and "sensor and actuator interface" functions (if any). A configuration contains one or more resources, each of which contains one or more programs executed under the control of zero or more tasks. A program may contain zero or more function blocks or other language elements as defined.
Configurations and resources can be started and stopped via the "operator interface", "programming, testing, and monitoring", or "operating system" functions. The starting of a configuration shall cause the initialization of its global variables according to the standard, followed by the starting of all the resources in the configuration. The starting of a resource shall cause the initialization of all the variables in the resource, followed by the enabling of all the tasks in the resource. The stopping of a resource shall cause the disabling of all its tasks, while the stopping of a configuration shall cause the stopping of all its resources.
Programs, resources, global variables, access paths (and their corresponding access privileges), and configurations can be loaded or deleted by the "communication function". The loading or deletion of a configuration or resource shall be equivalent to the loading or deletion of all the elements it contains.
Access paths and their corresponding access privileges are defined in this standard.
The mapping of the language elements defined in this subclause onto communication objects is defined in IEC 1131-5.

## Slide 9: Function Blocks in the IEC 61804 Context (Scheduling View)
Notes: The basic high-level language elements and their interrelationships are illustrated above. These consist of elements which are programmed using the languages defined, that is, programs and function blocks; and configuration elements, namely, configurations, resources, tasks, global variables, and access paths, which support the installation of programmable controller programs into programmable controller systems.
A configuration is the language element which corresponds to a programmable controller system. A resource corresponds to a "signal processing function" and its "man-machine interface" and "sensor and actuator interface" functions (if any). A configuration contains one or more resources, each of which contains one or more programs executed under the control of zero or more tasks. A program may contain zero or more function blocks or other language elements as defined.
Configurations and resources can be started and stopped via the "operator interface", "programming, testing, and monitoring", or "operating system" functions. The starting of a configuration shall cause the initialization of its global variables according to the standard, followed by the starting of all the resources in the configuration. The starting of a resource shall cause the initialization of all the variables in the resource, followed by the enabling of all the tasks in the resource. The stopping of a resource shall cause the disabling of all its tasks, while the stopping of a configuration shall cause the stopping of all its resources.
Programs, resources, global variables, access paths (and their corresponding access privileges), and configurations can be loaded or deleted by the "communication function". The loading or deletion of a configuration or resource shall be equivalent to the loading or deletion of all the elements it contains.
Access paths and their corresponding access privileges are defined in this standard.
The mapping of the language elements defined in this subclause onto communication objects is defined in IEC 1131-5.

## Slide 10: Basic Concepts of IEC 61499
Distributed applications
Event and data interfaces
Software encapsulation and reuse
Event-driven state machines
Service interfaces
Management services
Software portability

## Slide 11: Distributed Applications
Event flow
Data flow
Communication network(s)
Device 2
Device 3
Device 4
Device 1
Application A
Appl. C
Application B
Controlled process

## Slide 12: Event and Data Interfaces
Data outputs
Data inputs
Event outputs
Event inputs
Data flow
Event flow
Event/Data
Associations
Event flow
Data flow

## Slide 13: Software Encapsulation and Reuse in IEC 61131-3
Control Algorithm Specification
External Interface Specification
IN
BOOL
DB_TIME
TIME
OUT
BOOL
DEBOUNCE
DB_FF
S1
R
Q1
OFF_TMR
TON
IN
PT
Q
ET
OUT
DB_TIME
IN
IN
PT
Q
ET
TON
ON_TMR
SR
or
IN
PT
Q
ET
TON
OFF_TMR
ON_TMR
TON
IN
PT
Q
ET
| |
IN
|/|
IN
(R)
OUT
(S)
OUT
DB_TIME
DB_TIME
Notes: The primary encapsulation mechanism defined within the IEC PLC Programming Languages standard is the Function Block.
The function block can be thought of as an External Behavior Specification and an Internal Behavior Specification. The users of function blocks need only concern themselves with the external behavior and are isolated form in internal behavior of the function blocks. This is a useful tool for encapsulation of frequently used tasks in a system. For instance a switch debounce algorithm may be designed once and used many times in a user program. Using this principal the user can continue to encapsulate increasing levels of functionality until a suitable level is achieved.

## Slide 14: Software Encapsulation and Reuse in IEC 61499: Basic Function Block Types
Output variables
Input variables
EI variables
Control
Execution
Chart
EO variables
Algorithms
Type identifier
(IEC 1131-3)
Internal
variables

## Slide 15: Software Encapsulation and Reuse in IEC 61499: Composite Function Block Types
Output variables
Input variables
Event inputs
Event outputs
Type identifier
Execution Control
Functional composition
Reusable
Atomic (not distributable)

## Slide 16: Software Encapsulation and Reuse in IEC 61499: Adapter Interfaces
adapter connection
EI
EO
DI
DO
EI
EO
DI
DO
provider
acceptor
socket
plug
Reduce diagram clutter
Simplify transducer interface
Capture patterns of interaction

## Slide 17: Event-Driven Execution Control
Execution control
function
Scheduling function
Algorithm
2
8
1
5
4
6
3
7
= sampling

## Slide 18: The Execution Control Chart (ECC): An Event-Driven State Machine

## Slide 19: IEC 61499 Device Model
Device = Container for Resources
Device provides Communications & Process Interfaces
Communication link(s)
Resource x
Controlled process
Resource z
Resource y
Application B
Application C
Application A
Device boundary
Communication interface(s)
Process interface(s)
Notes: Communication and process interfaces are explicitly modeled in the TC65/WG6 device model. The resource provides the execution environment for the control algorithms specified by the function block diagrams contained in the application. Communication between function blocks in an application is modeled implicitly by signal connections. Communication between applications is modeled explicitly by communication function blocks; similarly, process interfaces are modeled explicitly by I/O function blocks.

## Slide 20: IEC 61499 Resource Model
Resource schedules & executes FB algorithms
Resource maps Communications & Process I/O Functions to Service Interface Function Blocks
Function
Block
Local application
(or local part of distributed application)
Communication mapping
Communication functions
Process I/O functions
Process mapping
Data
Events
Service
Algorithm
Scheduling Function
Interface
Function
Block
Service
Interface

## Slide 21: Service Interface Function Blocks
Access to Resource functionality
Modeled as sequences of service primitives per ISO/IEC TR8509
(application-initiated transactions)
(resource-initiated transactions)
t

## Slide 22: Communication Service Interfaces: Publish/Subscribe Model
INITO(+)
PARAMS
INITO(+)
INIT(+)
PARAMS
INIT(+)
~
~
CNF(+)
SD_1, ..., SD_m
RSP(+)
REQ(+)
IND(+)
RD_1, ..., RD_m
BOOL
QO
ANY
STATUS
PARAMS
ANY
FB_PUBLISH
SD_m
ANY
QI
BOOL
:
:
SD_1
ANY
EVENT
CNF
REQ
EVENT
INIT
EVENT
EVENT
INITO
BOOL
QO
ANY
STATUS
FB_SUBSCRIBE
:
:
INIT
EVENT
EVENT
INITO
RSP
EVENT
EVENT
IND
QI
BOOL
ANY
RD_m
ANY
RD_1
PARAMS
ANY

## Slide 23: Communication Service Interfaces: Client/Server Model
INITO(+)
INITO(+)
PARAMS
INIT(+)
PARAMS
INIT(+)
CNF(+)
SD_1, ..., SD_m
RSP(+)
REQ(+)
IND(+)
RD_1, ..., RD_m
SD_1, ..., SD_n
RD_1, ..., RD_n
BOOL
QO
ANY
STATUS
FB_CLIENT
SD_m
ANY
:
:
QI
BOOL
:
:
SD_1
ANY
ANY
RD_n
ANY
RD_1
EVENT
CNF
REQ
EVENT
INIT
EVENT
EVENT
INITO
PARAMS
ANY
BOOL
QO
FB_CNXN_STATUS
STATUS
PARAMS
ANY
FB_SERVER
SD_n
ANY
:
:
INIT
EVENT
EVENT
INITO
RSP
EVENT
EVENT
IND
QI
BOOL
:
:
SD_1
ANY
ANY
RD_m
ANY
RD_1

## Slide 24: A Device Management Service Interface
Command syntax examples:
  CREATE functionBlockInstance
  CREATE functionBlockType
  QUERY dataTypeName
  CREATE connection
  START functionBlockInstance
  STOP functionBlockInstance
  DELETE connection
  DELETE functionBlockInstance

## Slide 25: A Remote Device Management Model

## Slide 26: System Management Model

## Slide 27: Open Distributed Systems: The IEC 61499 Vision
Project Repository
Engineering Toolsets
DeviceNet EDSs Fieldbus DDs etc.
Libraries:
IEC 61915 IEC 61499 IEC 61131-3 Application Frameworks
import
XML
PORTABILITY
Standard management protocols: CONFIGURABILITY
Standard data transfer protocols: INTEROPERABILITY
Distributed intelligent devices & controllers
KEY:
Existing & Normative in IEC 61499 Existing but non-Normative in IEC 61499
To be done

## Slide 28: Engineering Tool Models

## Slide 29: IEC Project 61499 Status & Future
IEC 61499-1, Architecture
  PAS (Publicly Available Standard) Draft Complete, 2000-04-01
IEC 61499-2, Engineering Task Support
  2nd CD (Committee Draft) Completed
  PAS projected: 2000-07-01
2-year trial use period
  Incorporate lessons learned from trial implementations
  DIS projected: 2002-07-01
Home Page
  ftp://ftp.cle.ab.com/stds/iec/sc65bwg7tf3/html/news.htm